Twenty-high mill roll system storage, installation, use and maintenance

- Storage

- The new roller system or backing bearing should not be damaged inner box and stored in a box.

- Recycling roller bearings should be cleaned and coated with anti-rust oil for storage.

- The warehouse is dry, dust-free , and not damp.

- Dismantling

- The dismantling site is clean and dust-free.

- Remove the shaft end cover and remove the spacers or gears, saddles, keys, bearings, and other components in sequence. Do not remove the last gear or circlip. Place them in order for easy installation.

- The outer diameter end face of the bearing is numbered. It is not allowed to mix sleeves during disassembly. Pay special attention to the rolling elements. The middle row is long rollers.

- Installation

- The group of bearings should be cleaned before installation to remove oil, dust, and impurities.

- When the installation is difficult and needs to be knocked, use a copper hammer to hit lightly, not heavy hitting with iron.

- Remove burrs and foreign objects in related parts such as shafts, saddles, or roller boxes. Use a high-pressure air pipe to blow out impurities in the oil holes and check whether each oil hole is unblocked. Check the thickness of the bakelite thrust baffle, and replace it in time if it is too thin.

- The saddles and bearings of the same group should be installed in sequence numbering. The sequence numbers should not be confused. The heading of the saddle numbering faces the transmission side to avoid affecting the force condition. Pay attention to the position of the arrow on the end face of the bearing inner ring.

- On the machine again, the inner ring of the bearing should be rotated 90 degrees in the same direction to avoid the load area used last time, which is beneficial to improve the service life of the inner ring.

- After the bearing is installed, rotate each set of bearings by hand to check whether the bearing rotates flexibly and smoothly, and there must be no stuck, otherwise, it must be removed to check the cause of the failure.

- Before installation, check whether the surface of the plum blossom hole is smooth.

- The use of roller system

- When starting up and working, the lubrication system should be started first, and run for a few minutes.

- The lubricating oil must be clean and sufficient, and the flow rate and velocity must meet the indicators designed by the rolling mill.

- The roller system is used for one cycle (about 25 days), the bearing is removed from the machine for cleaning and inspection, and if any abnormalities are found, deal with it in time.

- When there are special situations such as tape breakage and tape sticking frequently, shorten the replacement time of the roller system and check whether the saddle bearing is damaged.

- The rolling process is reasonable and barbarous operation is avoided.

- The maintenance of the roller system

- The supporting roller system must be managed by a special person, and an account should be established. Record which set of saddles, which set of bearings, run-up time, run-off time, etc. on which rolling mill.

- The roller system must be shut down according to the cycle, regardless of whether there is a problem or not.

- After disassembly, check the roller system components one by one, and deal with the problems in time.

- The backing bearing must be parked for a period of time after the machine is repaired under the machine to continue using the machine again. Conditionally, after the bearing is removed from the machine or grounded, it is placed in 80°-100° oil for 24 hours to release stress.

- After the bearing has been used for a period of time, some pits, indentations, and other defects may appear on the outer diameter. At this time, the outer diameter should be re-ground in time. After re-grinding, it needs to be tested and re-matched before it can continue to be used. The amount of bearing grinding depends on the specific situation, and the grinding is mainly to ensure the T value and radial jump requirements of the same group. The dedicated instrument for measuring the T value of bearing section height.

- The bearing is not allowed to mix sets or sets during installation, disassembly, cleaning, and maintenance. It is not allowed to mix different bearing parts. Saddles are not allowed to be used in mixed groups.

- If there is a damaged bearing in a group of bearings, it is not allowed to arbitrarily match one to use, and the group should be tested and matched. The section height of the same group is less than 0.005mm, and the convexity is distributed.

- Avoid using a magnetic hoist to carry the roller system.

- Use new bearings or intact bearings for ABCD rollers as much as possible, but the bearings with some defects are used for EFGH rollers.

Wafangdian Guangda Bearing Manufacturing Co.,Ltd

Schematic diagram of T-value detection platform attached

- Backing bearings, when installing the bearings, install them according to the markings on the bearings, and group them before installing the inner ring.

- After the bearing is used for 300-350 hours, the load zone of the inner ring should be rotated by 90° or 120°, and the bearing must be re-ground after 1000 hours of use. Regroup optional H value.

3. The backing bearing is a high-precision bearing with strict matching. Each set of bearing

accessories shall not be mixed with other bearing accessories, and each group of bearings shall not be mixed with other groups.

4. There are 5 sets of bearings in each group, which are installed in sequence according to the bearing identification number during assembly.